## Slide 1: Optimal Dispatch of Reactive Power for Voltage Regulation and Balancing in Unbalanced Distribution Systems
Daniel Arnold
UC Berkeley and Lawrence Berkeley Lab
dbarnold@lbl.gov
Paper No: 16PESGM0464

## Slide 2: Background
OPF formulations for balanced systems utilize convex relaxations or approximations
Many approaches based on DistFlow and LinDistFlow models in seminal work of Baran and Wu1
Second order cone relaxations difficult to extend to 3 phase systems
Semidefinite relaxations fail to converge in many situations
Lack of suitable linearizations that relate voltages to complex power flows
[1] Mesut E Baran and Felix F Wu., “Optimal sizing of capacitors placed on a radial distribution system.”,
IEEE Transactions on Power Delivery, 4(1):735–743, 1989.

## Slide 3: Results
Developed a linearized model of unbalanced power flow that relates voltage magnitudes to complex power flows
LinDist3Flow - This approximation can be viewed as an extension of the LinDistFlow model to 3 phase systems
LinDist3Flow model allows problems to be addressed which hitherto could not be addressed with OPF techniques
Here, we incorporate the LinDist3Flow model into an OPF that uses reactive power resources to balance voltage magnitude across phases and provide voltage support
Simulations conducted on the IEEE 13 node feeder

## Slide 4: Conclusions/Recommendations
LinDist3Flow model is a good approximation for power flow equations in OPF formulations
Allows formulation of OPF approaches to enable new types of functionality:
  Voltage balancing (in this paper)
  3 Phase Voltage phasor reference tracking
  Stochastic OPF formulations